## Slide 1: Serial Communication Interface

## Slide 2: Outline
Serial vs Parallel Communication
Synchronous vs Asynchronous
Data Format
Baud rate
Register descriptions
Implementation Specific Features
Examples

## Slide 3: Introduction to Data Transmission
“transfer of data from point-to-point”
  http://en.wikipedia.org/wiki/Data_transmission
PURPOSE: It provides a method for electronic devices to communicate with each other
Ta Kim

## Slide 4: Parallel Data Transmission
N bits transmitted at a time over N data lines
Synchronization among all N bits
Note: each N bit is called a word
TRANSMITTER
RECEIVER
Ta Kim

## Slide 5: Serial Data Transmission
Transfers one bit at a time on one data line
TRANSMITTER
RECEIVER
Ta Kim

## Slide 6: Parallel vs. Serial
Parallel requires more transfer lines
Bits have to be synchronized
Fast, but expensive
Serial requires less transfer lines
Transfers one bit at a time
Slow comparatively, but less expensive
Ta Kim

## Slide 7: Bit Rate Comparison
Interface | Bit Rate (Mbits/sec) | Max. Cable Length (m)
Ultra-320 SCSI | 2560 | 12
P ATA | 1064 | 0.46 (18 in.)
S ATA | 1500 | 1
FireWire | 786 | 100
USB | 480 | 5
Parallel
Serial
Ta Kim

## Slide 8: Synchronous Serial Communication
Requires clock signal to synchronize transmitter and receiver
Continuous transmission to keep clock synchronized
Data transfer rate is determined by clock rate
Ta Kim

## Slide 9: Asynchronous Serial Communication
Transmitter and Receiver operate independently
  Transmitter sends data at any time
  Receiver is ready to accept data at all times
No need for clock signals
…but during transmission, format and transfer rate of data must match
Ta Kim

## Slide 10: Asynchronous Transmission
Word contains information that specifies the beginning and end of word to synchronize transmitter and receiver while exchanging data
Bit transfer rate is determined programmer (but also limited by interface) and must match between transmitter and receiver
Ta Kim

## Slide 11: Data Encoding Scheme
NRZ = Non-Return-to-Zero
  Uses a (+) voltage for 1
  Uses a (-) voltage for 0
Ta Kim

## Slide 12: Data Format
Start bit – indicates the beginning of word
Data bit – data user is transmitting
Parity bit – checks integrity of data
Stop bit – indicates the end of word
Ta Kim

## Slide 13: Data Format
Idle 1
Start bit 0
Data bit 0 or 1
Parity 0 or 1
Stop bit 1
Start
Bit
Data
Bit 0
Data
Bit 1
Data
Bit 2
Data
Bit 3
Data
Bit 4
Data
Bit 5
Data
Bit 6
Data
Bit 7
Parity
Bit
Stop Bit
HIGH
LOW
Idle
Ta Kim

## Slide 14: Example of Data Bit Formats
 | Start Bit | Data Bit | Parity Bit | Stop Bit
8 Bit Data Format | 1 | 8 | 0 | 1
 | 1 | 7 | 1 | 1
9 Bit Data Format | 1 | 9 | 0 | 1
 | 1 | 8 | 1 | 1
Ta Kim

## Slide 15: Parity
Hardware supports both odd and even parity
When enabled, MSB is parity bit
Even Parity
  Parity bit is set to 1 when the number of 1 bits is an odd number (when including the parity bit, is then even)
Nick Earnhart

## Slide 16: Parity
Odd Parity
  Parity bit is set to 1 when the number of 1 bits is even (when including the parity bit, is then odd)
Example – Even Parity
  0101010101 4 1’s in data  0
Data
Start Bit
Stop Bit
Parity Bit
Nick Earnhart

## Slide 17: Error and Issues
Noise Detection
Overrun
Framing Error
Parity Error
Nick Earnhart

## Slide 18: Noise Detection for Start Bit
NOT the same frequency as the bus clock
RT Clock = baud rate * 16
Nick Earnhart

## Slide 19: Noise Detection for Start Bit
Samples taken after the signal falls to 0 to verify if it is indeed a start bit
RT3, RT5, RT7 are samples taken
If two “1”s in sample, then flagged & not a start bit
Nick Earnhart

## Slide 20: Overrun
Software fails to read the SCI data register before it receives the next frame
RECEIVER
REGISTER
SOFTWARE
TRANSMITTER
Nick Earnhart

## Slide 21: Framing Error
Data sent are not in proper format
  Start bit is indicate the beginning of each frame and a reference point for the other bits in the frame
  Stop bit is not where it’s expected to be
TRANSMITTER
RECEIVER
FORMAT RECIEVER EXPECTS
FORMAT TRANSMITTER SENDS
Nick Earnhart

## Slide 22: Parity Error
Data sent are not in proper format
  Parity bit does not match with what is expected
Example:
  Transmitter is sending #$99
  Not set up with same parity as receiver
TRANSMITTER
RECEIVER
0
1
0
0
1
1
0
0
1
0
0
0
1
0
0
1
1
0
0
1
1
0
Nick Earnhart
What it gets…
What it thinks it should get…

## Slide 23: Baud & Bitrate
Baud rate and bit rate are NOT the same
Baud rate (Bd) is the number of line state changes possible per second
Bit rate (bps) is the number of bits transmitted per second
The hardware we are using has two line states (high/low)
Two line states can be represented with one bit
In our hardware, 1 baud = 1 bit
Nick Earnhart

## Slide 24: Baud & Bitrate
Other hardware can produce and recognize more than two line states using voltage, frequency, or phase modulation resulting in more bits per baud
bps = baud rate x number of bits per baud
In our hardware, given a 9600 baud rate
Nick Earnhart

## Slide 25: Baud & Bitrate
Not all bits transmitted are data
Start/stop/parity bits are transmission overhead
Throughput = data transmission excluding overhead
A useful unit for describing throughput is characters per second (cps)
A standard character is one byte of data
  cps is not the same as bytes per second
  bytes per second is ambiguous on whether overhead is subtracted out or not.
Nick Earnhart

## Slide 26: Baud & Bitrate
Assuming 9600bd line speed, 8 bit data format with no parity, 1 start bit and 1 stop bit, calculate the throughput in cps using the following equation
Nick Earnhart

## Slide 27: Baud & Bitrate
Assuming 9600bd line speed, 8 bit data format with no parity, 1 start bit and 1 stop bit, calculate the throughput in cps using the following equation
Don’t forget to convert bauds to bits per second first!
Nick Earnhart

## Slide 28: Baud & Bitrate
Baud set by the equation:
Where BR is the content of Baud Rate Register (described later)
Value 0 to 8191
Serial communication uses only 2 line states thus Bd = bps
Nick Earnhart

## Slide 29: Baud & Bitrate
Table with sample Baud Rates
Can’t always get the exact baud rate due to division of the clock
Nick Earnhart

## Slide 30: Implementation Specific Features (S12SCIV2)
Full Duplex
13-bit baud rate selection
8- or 9-bit data format
Separate TxD and RxD enable
Programmable output parity and Hardware parity checking
Two receiver wake up methods
Interrupt driven operation with 8 flags
8 registers used to control SCI ($00C8-$00CF)
Uses Port S pins 0 & 1 for RXD and TXD respectively
Razid Ahmad

## Slide 31: Register descriptions
Key settings will be discussed in detail
Safe to use defaults for all other settings
Summarizes pages 383-393 in Family Reference Manual
Razid Ahmad

## Slide 32: $00C8/C9 – SCIBDH/SCIBDL
13-Bit register determines SCI Baud rate
Baud rate generator is Disabled until TE or RE bit is set after reset.
You MUST write to SCIBDH and then SCIBDL.
Baud rate generator is turned off when this register contains $0000
Razid Ahmad

## Slide 33: $00CA – SCICR1
M (data format mode) – 0: 8-bit, 1: 9-bit. Both 8- and 9-bit data have 1 start and 1 stop bit.
PE (parity enable) – 0: OFF, 1: ON
PT (parity type) – 0: EVEN, 1: ODD
Razid Ahmad

## Slide 34: $00CB – SCICR2
TIE (transmit interrupt enable) – 0: disables interrupts for transmit data register empty, 1: enables
TCIE (transmit complete interrupt enable) – 0: disables interrupts for transmit complete, 1: enables
RIE (receiver interrupt enable) – 0: disables interrupts for receiver full and overrun , 1: enables
Razid Ahmad

## Slide 35: $00CB – SCICR2
ILIE (idle line interrupt enable) – 0: disables interrupts for idle line, 1: enables
TE (transmit enable) – 0: disable transmitter, 1: enable
RE (receiver enable) – 0: disable receiver, 1: enable
Razid Ahmad

## Slide 36: $00CC – SCISR1
Read only
TDRE (transmit data register empty) – 1: byte successfully transferred to transmit shift register
TC (transmit complete) – 0: no transmit in progress, 1: transmit in progress
RDRF (receive data register full) – 0: no data in SCIDRL, 1: data in SCIDRL
Razid Ahmad

## Slide 37: $00CC – SCISR1
OR (overrun) – 0: no overrun, 1: overrun (overrun happens when new data is received before old data is read)
NF (noise flag) – 0: disable, 1: enable
FE (framing error flag) – 0: disable, 1: enable
PF (parity error) – 0: No parity error, 1: parity error
Razid Ahmad

## Slide 38: $00CD – SCISR2
Not a very interesting register
TXDIR (transmitter pin direction) – 0: TXD pin used as input, 1: TXD pin used as output. (used only in single wire mode)
Razid Ahmad

## Slide 39: $00CE/CF – SCIRDH/SCIRDL
SCIRDL contains incoming bytes of data from serial port
R8 – bit 8 of received 9-bit data
T8 – bit 8 of transmitted 9-bit data
Razid Ahmad

## Slide 40: SCI is easy
SCI module makes it easy to send/receive data
SCI module encodes data into standard NRZ format!
Hardest part is setting up baud rate
Can use either flag based or interrupt based logic to drive SCI
  One interrupt vector associated with all 8 flags
SCIDRH/SCIDRL are like two registers in one.
  Read this register to receive data
  Write to this register to send data
Razid Ahmad

## Slide 41: Example
First, calculate baud rate. Assume 8MHz bus and desired baud rate is 9600
SCI module runs at bus speed
Razid Ahmad

## Slide 42: Example
First, calculate baud rate. Assume 8MHz bus and desired baud rate is 9600
SCI module runs at bus speed
Desired value for SCIBR is 52
You will have some error margin
  Exact solution is 52.0833
  Actual baud rate is 9615.3 (0.160% error)
Razid Ahmad

## Slide 43: Example
Write SCIBR ($34) to SCIBDH/SCIBDL
For 8-bit, no parity, no interrupts, default values will work
Simply enable transmit and receive in SCICR2
Read from SCIDRL to receive 8-bit data
Write data to SCIDRL to send 8-bit data
Program will do a remote echo
Razid Ahmad

## Slide 44: Code Example
Razid Ahmad

## Slide 45: Code Example
Razid Ahmad

## Slide 46: References
MC9S12C Family Reference Manual
Previous semester slides
Wikipedia

## Slide 47
#include <hidef.h> /* common defines and macros */
#include <mc9s12c32.h> /* derivative information */
#pragma LINK_INFO DERIVATIVE "mc9s12c32"
void SCI_init(void){
int BR = 0x34;
SCIBDH = (unsigned char)(BR>>8); //stores high Byte
SCIBDL = (unsigned char)(BR); //stores low Byte
SCICR2 = 0x0C; //sets TE and RE to 1
}
unsigned char SCI_getByte(void){
while (!(SCISR1_RDRF))
;//waits FOREVER until receive register is full
return SCIDRL;
}
void SCI_sendByte(unsigned char data){
while (!(SCISR1_TDRE))
;//waits FOREVER until transmit register is empty
SCIDRL = data;
//return void;
}
void main(void) {
//variable declarations must go at beginning
/* put your own code here */
EnableInterrupts;
//required code as per instructions
MISC = 0x03;
PEAR = 0x0C;
MODE = 0xE2;
//Call function to setup SCI
SCI_init();
//Main loop
for(;;) {
SCI_sendByte(SCI_getByte());
} /* wait forever */
/* please make sure that you never leave this function */
}